BlobPlot2 Documentation

Variables

All variables are denoted as follows:-

U8 for Unsigned Int8.
I8 for Signed Int8.
U16 for Unsigned Int16.
I16 for Signed Int16.

$0420	BLOB_Mode_U8	Bit-field of mode bits for plotting. See Table 1.
$0421	BLOB_X_U8	X co-ordinate for plotting the selected blob.
$0422	BLOB_CurrBlob_X_U8	Current blob x co-ordinate (used internally).
$0423	BLOB_Y_U8	Y co-ordinate for plotting the selected blob.
$0424	BLOB_CurrBlob_Y_U8	Current blob y co-ordinate (used internally).
$0425	BLOB_BaseAddr_U16	Base address for storage of blobs.
$0427	BLOB_CurrBlob_U8	Current blob number, starting at 0.
$0428	BLOB_XoffsetV_I8	Used internally for blob pixel placement in X direction.
$0429	BLOB_YoffsetV_I8	Used internally for blob pixel placement in Y direction.
$0430	BLOB_MaskBit_U8	Used internally for blob pixel selection.

Calls

There is only one call, and the code is relocatable

BLOB_Plot	Load address.

Table 1. Bit-field for BLOB_Mode_U8

- Bit 0:	BLOB_ModeSet_Cb. Set pixels when a 1 is found.
- Bit 1:	BLOB_ModeClr_Cb. Clear pixels when a 0 is found.
- Bit 2:	BLOB_ModeInv_Cb. Inverts the sprite data as read. Doesn’t affect the blobs.
- Bit 3:	BLOB_ModeXRev_Cb. Reverse the X axis.
- Bit 4:	BLOB_ModeYRev_Cb. Reverse the Y axis.
- Bit 5:	Not used.
- Bit 6:	Not used.
- Bit 7:	Not used.